## Slide 1: DREAM Preterm Birth Prediction Challenge
Luka Erdeljanović
2020/3381
Genome informatics

## Slide 2: Challenge Description
Construct a machine-learning model which can predict the gestational age based on gene expressions from blood samples
Select a batch of genes which is of most interest for the prediction
Evaluate the model using a set of metrics for regression and K-fold cross-validation
More details: DREAM Preterm Birth Prediction Challenge

## Slide 3: Input Data
735 samples in total
367 samples for training, the rest for validation
Over 32,000 gene expressions in each
Conclusion: sparse data, huge number of input variables – identify most relevant genes

## Slide 4: Data Pre-processing and Model Setup
Work performed using Python’s SciKit Learn, Numpy and Pandas
Grab the most important features using SciKit’s SelectKBest feature selection
  Empirically set K=8,000 out of a total of over 32,000 features
  Potential improvement point: identify and remove outliers in the samples and improve the selection of K (run more tests with different values).
Create models – Linear regression is the base model in a number of different setups

## Slide 5: Linear Regression models
SciKit’s default LinearRegression model (min. Residual Sum of Squares)
Ridge regression (Linear Regression with Tikhonov/L2 regularization)
  In theory: should be used with large amount of features which have balanced effect on the outcome
Lasso regression (Linear Regression with L1 regularization)
  In theory: should be used with small amount of features which have a large impact on the outcome; less robust on outliers than L2
These models were run in 2 variants – normalized data and default data
Number of different learning gradients (alpha) used for regularization:
  0.0001, 0.001, 0.01, 0.1, 0.5, 1, 10, 100, 1000, 10000

## Slide 6: Linear Regression Basics
Hypothesis – our mathematical representation:
Error and Loss function:
Find the minimum:
Up to 100.000 iterations

## Slide 7: Learning Process
Chart: Learning Process
Real Values | 5 | 3 | 5 | 6 | 6 | 3 | 4 | 8 | 9 | 11 | 7 | 8 | 6 | 7 | 8 | 8
Prediction model | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Error metric

## Slide 8: Learning Process
Chart: Learning Process
Real Values | 5 | 3 | 5 | 6 | 6 | 3 | 4 | 8 | 9 | 11 | 7 | 8 | 6 | 7 | 8 | 8
Prediction model | 2 | 7 | 9 | 3 | 2 | 5 | 9 | 11 | 5 | 6 | 4 | 5 | 3 | 6 | 4 | 2

## Slide 9: Learning Process
Chart: Learning Process
Real Values | 5 | 3 | 5 | 6 | 6 | 3 | 4 | 8 | 9 | 11 | 7 | 8 | 6 | 7 | 8 | 8
Prediction model | 3 | 1.5 | 3 | 8 | 7 | 4 | 2 | 11 | 8 | 11 | 8 | 8 | 5 | 5 | 9 | 7
Error metric is minimized

## Slide 10: And Another Thing…
Regularization: we want to train our models for the real world, not the training data (prevent “overfitting”)
Normalized data: scale the input data down to the same level (e.g. from 0 to 1)

## Slide 11: Evaluation
K-Fold cross-validation used (10-fold)
  Split the data in 10 groups
  Train the models on 9 of the 10 groups [90% will be used for training, 10% for validation]
  Capture the performance of the models on the last group (validation)
  Now swap the validation group with one of the training groups
  Repeat 10 times so that each group is validated

## Slide 12: Evaluation Results – Training Data
Chart: 
| LinearReg Normalized | Lasso - Normalized - Alpha = 10000 | Ridge - Normalized - Alpha = 0.0001 | Lasso - Alpha = 1000 | Ridge - Alpha = 0.0001 | Ridge - Normalized - Alpha = 10000 | LinearReg | Ridge - Alpha = 10000 | Lasso - Alpha = 0.0001 | Lasso - Normalized - Alpha = 0.001
RMSE training | 4.2308 | 8.0701 | 4.2313 | 4.5321 | 4.5326 | 5.6378 | 5.6746
RMSE testing | 9.619 | 8.1088 | 8.1088 | 8.111 | 10.1111 | 8.4627 | 10.614

## Slide 13: Conclusions
“Normalizing” data is critical, as is the adequate selection of features
Training and reality are different - and might trick you!
Potential improvements could be made
  Better handling of data (perhaps stratification?)
  Removing outliers
  Bigger training sets (of course)
  Mixing the data differently (not allowed, but would be interesting…)

## Slide 14: Thank you
Questions?
luka.erdeljanovic@gmail.com
github.com/cypher93/genomska_informatika